## Slide 1
CCP-LAW
Curricula development on Climate Change Policy and Law
Project No of Reference: 618874-EPP-1-2020-1-VN-EPPKA2-CBHE-JP:
The European Commission's support for the production of this publication does not constitute an endorsement of the contents, which reflect the views only of the authors, and the Commission cannot be held responsible for any use which may be made of the information contained therein.
Subject title: Topic 2_The Science of Climate Change and Waste
Author: Filio Petridou_ PEDMEDE

## Slide 2
Contents
1. The Science of Climate Change and Waste Management………………………….
2. Understanding the Greenhouse Effect and Carbon Footprint………………………..
3. The impact of Climate Change and Waste on ecosystems and biodiversity……..
Reference List………………………………………………………………………………………

## Slide 3
1. The Science of Climate Change and Waste Management
  Climate change means the change of climate over the last 100 years which is caused directly or indirectly by human activities.
  Mainly, climate change represents the changes in long-term weather patterns. Usually, climate change is measured in a shift of temperature, rainfall, wind pattern, or more.
  World’s temperature has increased by 0.7⁰C since the industrial era.
  The rise in temperature has been linked to an increase in the concentration of greenhouse gases in the earth’s atmosphere.

## Slide 4
1.1 Focus on human impact
The primary cause of climate change is the variation of the solar radiation retained by the earth’s surface.
Other occasional factors which may lead to short-lived climatic variations include volcanic eruptions,
variation in solar outputs,
variation in orbital characteristics and variation in atmospheric CO2.
Apart from variation in atmospheric CO2, the other factors, to a large extent, are independent of anthropogenic factors (Nnaji& Utsev, 2011).

## Slide 5
1.1.1 Anthropogenic Factors
Increase in greenhouse gases in the atmosphere. For instance, CO2, Nitrous oxide and Ozone.
Burning of fossils produces a great amount of CO2 emissions.
Combustion of coal and petroleum for power generation.
Manufacturing of one tonne of cement can produce half a tonne of CO2.
Release of methane gas due to both anthropogenic and natural causes.
Release of nitrous oxide due to the use of fertilizers.
Industrial development has resulted in manifold environmental problems at local, regional and global levels.
Overexploitation of natural resources causes reduction of forest, land degradation, lowering of groundwater table, etc.
Toxic and hazardous substances discharged into the water bodies adversely affect the aquatic ecosystem and biotic community.
The urbanization changes the radiation and heat balance in the local atmosphere.
Urbanization affects the local climate through the formation of heat islands, the creation of pollution dome above the city and alteration of the hydrological regime, etc.
Due to decreased water availability, crop yield would be reduced in most of the tropical and sub-tropical regions.

## Slide 6
1.2 Is climate change a waste management problem?
  The physical problem underlying climate change is very simple: dumping carbon dioxide and other greenhouses gases into the air raises their concentrations in the atmosphere and causes gradual warming.
  Till now the most common strategy was that the world must radically reduce carbon-carrying gases emissions.
  Nevertheless, carbon dioxide is a waste product; dumping it into the open air is a form of littering, therefore dumping can be avoided or cleaned up with technological fixes to the current infrastructure.
  These fixes do not require drastic reductions in energy use, changes in lifestyle, or transformations in energy technologies. Keeping carbon dioxide out of the atmosphere is a waste management problem.
  The rapid mixing of carbon dioxide in the atmosphere simplifies this waste management problem compared with others, such as sewage or municipal garbage, because it does not create local damage, and it does not matter where carbon dioxide molecules are removed from the atmosphere as long as the amount removed equals the amount added.
  For global climate change, a change in primary focus from emissions reduction and resource conservation to waste disposal changes the approach to the carbon problem.

## Slide 7
The focus on carbon cycle to address climate change
Since 1950, human activity has been producing more GHGs than the Earth can absorb, and this is when man-made climate change can be said to have started.
In 1950 there was 311.79 PPM of CO2 in the atmosphere. In 2021 that had risen to 416.45 PPM. So in 1950, there was only 74.86% as much CO2 in the atmosphere as we have currently.
Around 25% of the total CO2 in the atmosphere is contributing to climate change.

## Slide 8
Key facts
Waste generation rate indicates positive agreement with
per capita power usage,
The world emits around
47.5 Billion Tons of greenhouse gas every year, 34.73
Whilst it is not the most potent gas, the volume of CO2, currently accounting for
66% of the effects of climate change
gross domestic product (GDP) and
end user’s consumption
Billion Tons of which are carbon dioxide
The energy sector accounts for
75.6% of global greenhouse gas emissions

## Slide 9
Carbon dioxide waste management approach
Doesn’t demand a radical shape of production and lifestyle or
a major transformation in existing energy infrastructures and technologies or
a coordination between existing energy infrastructures and technologies (Lackner and Christophe, 2017)
Direct and indirect (i.e., via conversion) utilization of CO2, alternative to gaseous CO2 (Sharifian, et. Al, 2021).

## Slide 10
Contribution of Waste Management Options to Global Warming
Nnaji& Utsev, 2011

## Slide 11
Dominant non-electrochemical CO2 capture methods
Capture method | Process mechanism | Challenges
Oxy-fuel | Instead of air, pure O2(g) or a CO2(g)/O2(g) mixture is used for fuel combustion. 75–80% CO2 is produced as opposed to combustion in normal air where 3–15% CO2 is produced | • High oxygen production energy costs (ca. 200–220 kW h per tonne of oxygen generated by cryogenic air separation)
 |  | • High sensitivity to air leakage into the system
 |  | • Although an efficient capture method, difficult to retrofit compared to post-combustion method
 |  | • Special materials are needed to resist the high flame temperature (ca. 3500 °C). Although, the recycled CO2 can be used to moderate this temperature
Pre-combustion | CO2 is separated from H2-rich fuel before combustion. For example, synthetic gas is produced from fossil fuel by adding steam or pure oxygen at high temperature and pressure (1400 °C and 25–55 atm) and a subsequent water–gas shift reaction. | • Retrofit to existing plants is costly and more difficult compared to oxy-fuel and post-combustion
 |  | • Reaction CO + steam ↔ CO2 + H2 produces 15–40% CO2 at 14–40 atm. The produced H2 can be used for power generation, but CO2 needs to be removed using a subsequent separation technique
Post-combustion: |  | 
Absorption | CO2(g) (from flue gas or air) is absorbed (i.e., chemically or physically) in an absorbent. Pure CO2(g) is subsequently recovered through temperature swing desorption while the absorbent will be regenerated. Currently, amine based capture is the most mature method for CO2 capture | 
Sharifian et al. (2021)

## Slide 12
Electrochemical CO2 capture methods
Sharifian et al. (2021)

## Slide 13
2. Understanding the Greenhouse Effect & Carbon Footprint
Greenhouse Gas (GHG) Emissions
Major Greenhouse gases
Water vapour– One of the biggest contributors of greenhouse effect.
Carbon dioxide– It is the primary greenhouse gas emitted through anthropogenic activities.
    Main sources of CO2
    Combustion of fossil fuels for electricity generation.
    Combustion of fossils for transportation.
    Industrial processes.
Combustion of mineral products such as cement, the production of metals, etc.
Methane- The wetlands are the largest sources of methane emissions. Domestics cattle produce a large amount of methane during digestion. Agriculture is the primary source of Methane emissions.

## Slide 14
Nitrous oxide- It is naturally present in the atmosphere. As it is the part of the nitrogen cycle. Fertilizers emit a large amount of nitrous oxide in the atmosphere. Transportation fuels also emit nitrous oxide.
Fluorinated gases- These gases are produced through a variety of industrial processes. For instance, the manufacturing of aluminium and semiconductors. These gases are of three types as following
    Hydrofluorocarbons (HFCs)
    Perfluorocarbons (PFCs)
    Sulphur hexafluoride (SF6)
Aerosols- These are also known as black carbon. They contribute to the warming of the atmosphere. The major sources of black carbon are as following:
Biomass burning
Cooking with solid fuels
Diesel exhausts, etc.

## Slide 16
The single biggest contributor to man-made greenhouse gas emissions is burning fossil fuels - coal, oil, and natural gas.
Carbon dioxide accounts for around 75% of GHG emissions caused by human activity, and fossil fuels are the primary cause of CO2.
The Annual Greenhouse Gas Index (AGGI) is a way of measuring how much influence the different GHGs have on climate change. It uses a metric known as Global Radiative Forcing which essentially multiplies the amount of each GHG in the atmosphere by the effect per part that each gas has, in order to determine its overall contribution to global warming.
Based on the latest 2021 AGGI data, carbon dioxide is responsible for 2.14 of the total 3.222 Global Radiative Forcing, meaning that currently, CO2 causes 66% of global warming.

## Slide 17
Causes of Greenhouse Gas Emissions
The EPA, UN, and EU all agree that the major causes of global warming/climate change are as follows:
    Carbon dioxide emissions from the burning of fossil fuels.
  Deforestation, which destroys the trees and forests which can help to remove CO2 from the atmosphere.
Livestock farming which leads to increased numbers of cattle and sheep, both of which produce large quantities of methane.
Using chemical fertilizers that contain nitrogen, resulting in emissions of nitrous oxide.
Fluorinated gases which are used in a variety of household and industrial appliances, notably refrigeration equipment, air conditioning and heat pumps.
All of the above causes are a result of human activities.
What are the top 5 causes of global warming?

## Slide 18
Top sources of GHG emissions
The primary source of greenhouse gas emissions is the energy sector.
The latest CAIT climate watch data shows that energy accounts for 75.6% of total global GHG emissions. This has remained stable in percentage terms over the past 5 years.
Electricity and heating produce the most greenhouse gas emissions, being responsible for 15.83 Gigatons CO2e (carbon dioxide equivalent) or 42.1% of the total.
Transportation is the second-largest subsector, producing 8.43 Gt or 22.4%.

## Slide 19
Sharifian et al. (2021)
Carbon footprint
The calculated value or index to measure the total amount of greenhouse gases that an activity, product, company or country releases to the atmosphere.

## Slide 20
Geographical Distribution and Classification
Which country emits the most greenhouse gases?
China (10668 MtCO₂) followed by the United States (4713 MtCO₂) emits more carbon dioxide than any other country.
China’s coal consumption has increased its emission levels around 25% during the last decade.
China now produces more than twice as many emissions as the United States, which remains the second-largest emitter in the world.
Which country emits the least greenhouse gases? (less than 0.1 MMtCO2e)
Wallis and Futuna Islands
Montserrat
Niue
Saint Helena
Tuvalu
Which countries have net zero emissions or are carbon neutral?
Benin
Bhutan
Gabon
Guyana
Cambodia
Suriname
Which countries will achieve zero carbon emissions by 2050?
Canada
Germany
Denmark
Spain
Fiji
France
United Kingdom
Hungary
Ireland
Japan
South Korea
Luxembourg
New Zealand
Portugal
Sweden

## Slide 21
Source: Roundup.org
There were 416.45 parts per million of CO2 in the Earth’s atmosphere in 2021. This is an all-time high.
The amount of CO2 in the atmosphere has increased every year, since the 1950s, meaning we continue to produce more carbon dioxide than the earth can absorb. This makes a major contribution towards heating the planet.

## Slide 23
3. The impact of Climate Change and Waste on ecosystems and biodiversity
ECOSYSTEM STRESS
Ecosystems are harmed by physical, chemical and biological stressors.
The response to these stressors varies but depends on both the severity and amount of stress and the sensitivity of the ecosystem compartments to the stress.
Stressors can be:
i. a component of the environment that transfers the impact of a pressure (e.g. human activity) to other parts of the environment by being changed from its natural state (e.g. nutrient concentrations changed from natural, habitat coverage less than natural or excess salt). These components of the environment are usually present in natural (healthy) ecosystems and are only considered stressors when they are different from natural;
ii. a component of the environment that, when present, causes stress on the ecosystems (e.g. litter or pest species). These components of the environment are not usually present in natural (healthy) ecosystems and are considered potential stressors when they are present in any amount.

## Slide 24
Threats to global biodiversity and their impacts
Muluneh Μ., 2021

## Slide 25
Temporal and spatial qualities from exposure to a stressor
Muluneh Μ., 2021
Source: Vallero D. 2019

## Slide 26
Weather pattern and natural disasters
Extreme and unpredictable weather
Sea level rise
The melting of the glaciers, the polar ice cap and the Atlantic ice shelf are adding water to the ocean
Biodiversity
There has been a massive loss of biodiversity leading to initiation of the sixth mass extinction crisis
Crop productivity and human health
The loss in crop production from climate-driven abiotic stresses represents a major threat to global food security along with the decline of the nutritional value.
Increase in the frequency and intensity of natural disasters (floods, droughts, cyclones, hurricanes, typhoons, wildfires)
The volume of the ocean is expanding as the water warms.
Air pollution is considered to increase morbidity and mortality on public health causing
Increase in arboviral diseases such as zika fever, dengue and chikungunya
Increase in temperature impacts growth and development in plants and animals. A shift in distributional range of species and in phenological events.
Marine and aquatic ecosystems are affected by the extinction of a large number of endangered and endemic plant and animal species
Interlinkages between Climate Change and Ecosystems
Kundaranahalli Sh. (2022)

## Slide 27
Ecosystem Integrity
Waste generation rates have been positively correlated with per capita energy consumption, GDP, and final private consumption. Global solid waste generation rates range from 0.1-0.8t/cap/yr (tons per capita per year) in low-income countries, 0.2-0.5 t/cap/yr in middle-income countries and 0.3-0.8 t/cap/yr in high-income countries.
The integrity of ecosystems depends on proper waste management. This includes virtually
every waste stream (i.e. agricultural waste, solids of any form, construction, transportation, and municipal wastewater).
All the above harm the integrity of the receiving systems, by increasing turbidity, suspended and dissolved solids content, and the organic load. It may also contain constituents that can be inherently hazardous to humans, wildlife and other ecosystems.
Global heat map of per capita solid waste generation per day (kg/capita/d)
Source: Rajendran et al, 2019

## Slide 28
Evaluating Environmental Quality
Ecosystem Risk and Sustainability
Risk is the likelihood that an adverse effect will occur.
Sustainability is the likelihood that beneficial aspects will continue.
Source: Vallero D. 2019
Framework for integrated human health and ecological risk assessment

## Slide 29
Reducing the impact of waste management
Waste prevention
The climate benefits of waste avoidance and material efficiency far outweigh the benefits from any waste treatment technology, even when energy is recovered.
Recycling
Recycling saves on the use of raw materials, however recycling uses energy and often produces products of quality inferior to the primary product
Recovery
Waste serves a useful purpose by replacing other materials that would otherwise have been used to fulfil a particular function
Source: CIWEM.

## Slide 30
5R Waste Management System
The top-down versus the bottom-up approach
Source: Rajendran et al, 2019

## Slide 31
Efficiency of Waste Management Systems
Source: Rajendran et al, 2019
Multidimensional factors for an efficient waste management system

## Slide 32
Perspectives
A coherent intervention for sustainable waste management practices includes various stakeholders such as government, public, industries, scientists, and nongovernmental organizations.
Waste management is a multidimensional problem that needs localized solutions.
The important aspect of a sustainable waste management practice is the responsibility and political will to adopt and promote them.
Several countries (such as USA, Ireland, Sweden) have successfully implemented waste management technologies and are targeting to develop zero-waste cities. It is necessary for those countries to transfer that gained knowledge and experience to other countries for a sustainable world in the future.

## Slide 33
Reference List
Chaudhary, K. and Vrat P. Overview and Critical Analysis of National Law on Electronic Waste Management. Environmental Policy and La., 47(5-6). 181-188. 2017.
Kundaranahalli Sh. Climate change and its impact on biodiversity and human welfare. Proceedings of the Indian National Science Academy. 88. 10.1007/s43538-022-00073-6. 2022.
Lackner, K. S., and Christophe J. Climate Change is a Waste Management Problem. Issues in Science and Technology 33, no. 3. Spring 2017.
Ministry of Energy Transition. Key figures on climate France, Europe and Worldwide. France. December 2022. https://www.statistiques.developpement-durable.gouv.fr/edition-numerique/chiffres-cles-du-climat-decembre-2022/en/6--co2-emissions-excluding-lulucf. Access on 01.2024
Muluneh, M. Impact of climate change on biodiversity and food security: a global perspective—a review article. Agriculture & Food Security. 10. 10.1186/s40066-021-00318-5. 2021.
Nnaji, Ch. and Utsev, T. Climate Change and Waste Management: A Balanced Assessment. Journal of Sustainable Development in Africa. 13. 13 – 34. 2011.
Sharifian, R., Wagterveld, M., Digdaya, I., Xiang, Ch., Vermaas, D. Electrochemical carbon dioxide capture to close the carbon cycle. Energy & Environmental Science. 14. 2021.
Rajendran. K., Richen, L., Wall, D. M., Murphy, J. D. , Chapter 5 - Influential Aspects in Waste Management Practices, Editor(s): Mohammad J. Taherzadeh, Kim Bolton, Jonathan Wong. Ashok Pandey, Sustainable Resource Recovery and Zero Waste Approaches. Elsevier. 65-78. 2019
The Chartered Institution of Water and Environmental Management CIWEM. Waste Management and Climate Change. Policy Position Statement. https://www.ciwem.org/assets/pdf/Policy/Policy%20Position%20Statement/Waste-Management-and-Climate-Change.pdf. Access 01.2024.